## Slide 1: CS 356: Computer Network Architectures Lecture 9: Internetworking
Xiaowei Yang
xwy@cs.duke.edu

## Slide 2: Overview
Single-link networks
  Point-to-point links
  Shared media multiple access links
    Ethernet, token ring, wireless networks
  Encoding, framing, error detection, reliability
    Delay-bandwidth product, sliding window, exponential backoff, carrier sense collision detection, hidden/exposed terminals
Packet switching: how to connect multiple links
  Connectionless: Datagram
    Learning bridge algorithms
  Connection-oriented: Virtual circuits
  Source routing
  Pros and cons

## Slide 3: Today
Wrapping up switching technologies
  Asynchronous Transfer Mode (ATM)
  Switching hardware
New topic: how to connect different types of networks
  E.g., how to connect an Ethernet and an ATM network

## Slide 4: Review: Learning bridges
Automatic address learning
The spanning tree protocol

## Slide 5: Address Learning
Algorithm:
For each frame received, the bridge stores the source field in the forwarding table together with the port from which the frame was received
All entries are deleted after some time (default is 15 seconds).
  What if the host moved?

## Slide 6
Port 1
Port 2
Port 3
Port 4
Port 5
Port 6
Src=x, Dest=y
Src=x, Dest=y
Src=x, Dest=y
Src=x, Dest=y
Src=x, Dest=y
Src=x, Dest=y
x is at Port 3
Src=y, Dest=x
Src=y, Dest=x
Src=x, Dest=y
y is at Port 4
Src=x, Dest=y

## Slide 7: Building the Spanning Tree
LAN 2
Bridge1
LAN 5
LAN 3
LAN 1
LAN 4
Bridge2
Bridge5
Bridge4
d
Bridge3
D
D
D
R
D
R
R
R
D
Each bridges originally considers itself to be the root
Sends messages (root, root-cost, bridgeId, portID)
When it hears a better root or root-cost, updates its messages
When the protocol converges, the bridges have calculated the designated ports (D) and the root ports (R) as indicated.
  D: closest bridge to the root for a LAN
  R: port closest to the root

## Slide 8: Limitations of bridges
Scalability
  Broadcast packets reach every host!
Security
  Every host can snoop
Non-heterogeneity
  Can’t connect ATM networks

## Slide 9: Asynchronous Transfer Mode (ATM)
A fixed packet size network
Connection oriented
  Using signaling to setup a virtual circuit

## Slide 10: ATM Cells
Fixed-size packets
  5 bytes header
  48 bytes payload
If payload smaller than 48B, uses padding
If greater than 48B, breaks it

## Slide 11: Why small, fixed-length packets?
Cons: maximum efficiency 48/53=90.6%
Pros:
  Suitable for high-speed hardware implementation
  Many switching elements doing the same thing in parallel
  Reducing priority packet latency
    Good for QoS

## Slide 12
Reducing preemption latency

## Slide 13: Why 48 bytes
It’s from the telephone technology
Thought data would be mostly voice
A compromise
  US: 64 bytes
  Europe: 32 bytes
  (64+32) / 2 = 48 bytes

## Slide 14: Virtual paths
24-bit virtual circuit identifiers (VCIs)
  Discussed in our previous lecture
Two-levels of VCIs
  8-bit virtual path, 16-bit VCI
  Virtual paths shared by multiple connections

## Slide 15: Today
Wrapping up switching technologies
  Review learning bridges
  Asynchronous Transfer Mode (ATM)
New topic: how to connect different types of networks
  E.g., how to connect an Ethernet and an ATM network

## Slide 16: History of the Internet
Original design goal: Interconnecting different networks
Many different types of packet switch networks
  ARPANET, packet satellite networks, ground-based packet radio networks, and other networks.
Each has
  Hosts, packet switches, processes
  A protocol for communication
Q: what would you do differently given such a design task?

## Slide 17: Challenges
Different addressing schemes and host communication protocols
  Ethernet, FDDI, ATM
Different Maximum Transmission Units (MTUs)
Different success or failure indicators
End-to-end reliability: failures may occur at each network
Different control protocols
  Status information, routing, fault detection/isolation

## Slide 18: Inter-networking
Routers interface different networks
Uniform addressing (IP)
Routers send packets to their destination IP addresses

## Slide 19: Inter-networking design alternatives
Design alternative 1: one uniform technology
Design alternative 2: each host implements all other protocols
Notes: One uniform technology: too restrictive, cannot accommodate future technology development, too expensive to convert
Each host implements all other protocols: too expensive, does not scale

## Slide 20: Inter-networking design alternatives
Design alternative 1: one unified technology, a multi-media network
  Restrictive
  Not practical: existing networks can’t be connected
Design alternative 2: each host implements all other protocols
  Expensive
  Difficult to accommodate future development
Notes: Each host implements all other protocols: too expensive, does not scale

## Slide 21: Internet Protocol
IP (Internet Protocol) is a Network Layer Protocol
IP’s current version is Version 4 (IPv4). It is specified in RFC 791.

## Slide 22: IP: the thin waist of the hourglass
IP is the waist of the hourglass of the Internet protocol architecture
Multiple higher-layer protocols
Multiple lower-layer protocols
Only one protocol at the network layer.
What is the advantage of this architecture?
  To avoid the N * M problem

## Slide 23: Application protocol
IP is the highest layer protocol which is implemented at both routers and hosts
Application
TCP
IP
Data Link
Application
TCP
IP
Application protocol
TCP protocol
IP protocol
IP protocol
Data
Link
Data
Link
IP
Data
Link
Data
Link
IP
Data
Link
Data
Link
Data
Link
IP protocol
Router
Router
Host
Host
Data Link

## Slide 24: IP Service Model
Delivery service of IP is minimal
IP provides an unreliable connectionless best effort service (also called: “datagram service”).
  Unreliable: IP does not make an attempt to recover lost packets
  Connectionless: Each packet (“datagram”) is handled independently. IP is not aware that packets between hosts may be sent in a logical sequence
  Best effort: IP does not make guarantees on the service (no throughput guarantee, no delay guarantee,…)
Consequences:
Higher layer protocols have to deal with losses or with duplicate packets
Packets may be delivered out-of-order

## Slide 25: Basic IP router functions
Things you need to understand to do lab2
  Internet protocol
    IP header
    IP addressing
    IP forwarding
  Address resolution protocol
  Error reporting and control
    Internet Control Message Protocol

## Slide 26: Fields of the IP header
ToS (8-bit): specifies the type of differentiated services for a packet
HLen (4-bit): the length of header in 32-bit words
Length (16-bit): packet length in bytes, including the header
  65535 bytes
  Fragmentation and reassembly

## Slide 27: Fields of the IP Header
Identification (16 bits): Unique identification of a datagram from a host. Incremented whenever a datagram is transmitted (in some OS)
Flags (3 bits):
  First bit always set to 0
  DF bit (Do not fragment)
  MF bit (More fragments)
  Will be explained later Fragmentation
Fragment offset (13 bits)

## Slide 28: Fields of the IP Header
Time To Live (TTL) (1byte):
  Specifies longest paths before datagram is dropped
  Role of TTL field: Ensure that a packet is eventually dropped when a routing loop occurs
  Used as follows:
  Sender sets the value (e.g., 64)
  Each router decrements the value by 1
  When the value reaches 0, the datagram is dropped

## Slide 29: Fields of the IP Header
Protocol (1 byte):
    Specifies the higher-layer protocol.
    Used for demultiplexing to higher layers.
Header checksum (2 bytes): A simple 16-bit long checksum which is computed for the header of the datagram
  Function?

## Slide 30: Fields of the IP Header
Options:
    Record Route: each router that processes the packet adds its IP address to the header.
    Timestamp: each router that processes the packet adds its IP address and time to the header.
    (loose) Source Routing: specifies a list of routers that must be traversed.
    (strict) Source Routing: specifies a list of the only routers that can be traversed.
    IP options increase routers processing overhead. IPv6 does not have the option field.
Padding: Padding bytes are added to ensure that header ends on a 4-byte boundary

## Slide 31: Global IP addresses

## Slide 32: What is an IP Address?
An IP address is a unique global identifier for a network interface
  An IP address uniquely identifies a network location
Routers forwards a packet based on the destination address of the packet
Uniqueness ensures global reachability

## Slide 33: IP Addressing
Addressing defines how addresses are allocated and the structure of addresses
IPv4 (32-bit)
  Classful IP addresses (obsolete)
  Classless inter-domain routing (CIDR) (RFC 854, current standard)
IP Version 6 addresses (128-bit)

## Slide 34: An IPv4 address is often written in dotted decimal notation
Each byte is identified by a decimal number in the range [0…255]:
10001111
10000000
10001001
10010000
1st Byte
= 128
2nd Byte
= 143
3rd Byte
= 137
4th Byte
= 144
128.143.137.144

## Slide 35: Structure of an IP address
network prefix
host number
An IP address encodes both a network number (network prefix) and an interface number (host number).
  network prefix identifies a network
  the host number identifies a specific host (actually, an interface on the network).
The structure is designed to improve the scalability of routing
  Scales better than flat addresses
0
31

## Slide 36: How long is a network prefix?
Before 1993: The network prefix is implicitly defined (class-based addressing)
After 1993: The network prefix is indicated by a netmask

## Slide 37: Before 1993: Class-based addressing
The Internet address space was divided up into classes:
  Class A: Network prefix is 8 bits long
  Class B: Network prefix is 16 bits long
  Class C: Network prefix is 24 bits long
  Class D is multicast address
  Class E is reserved

## Slide 38: Classful IP Addresses (Until 1993)
Each IP address contained a key which identifies the class:
  Class A: IP address starts with “0”
  Class B: IP address starts with “10”
  Class C: IP address starts with “110”
  Class D: IP address starts with “1110”
  Class E: IP address starts wit “11110”

## Slide 39: The old way: Internet Address Classes

## Slide 40: The old way: Internet Address Classes

## Slide 41: Problems with Classful IP Addresses
Fast growing routing table size
  Each router must have an entry for every network prefix
  ~ 221 = 2,097,152 class C networks
  In 1993, the size of routing tables started to outgrow the capacity of routers
Local admins must request another network number before installing a new network at their site

## Slide 42: Solution: Classless Inter-domain routing (CIDR)
Network prefix is of variable length
  No rigid class boundary
Addresses are allocated hierarchically
Routers aggregate multiple address prefixes into one routing entry to minimize routing table size

## Slide 43: Hierarchical IP Address Allocation
American Registry for Internet Numbers (ARIN)
RIPE, APNIC, LACNIC, AfriNIC
Internet Assigned Numbers Authority
Regional Internet Registries
(Five of them)
Internet Service Providers

## Slide 44: CIDR network prefix has variable length
A network mask specifies the number of bits used to identify a network in an IP address.
10001111
10000000
10001001
10010000
11111111
11111111
1111111
00000000
128
143
137
144
255
255
255
0
Addr
Mask

## Slide 45: CIDR notation
CIDR notation of an IP address:
  128.143.137.144/24
  /24 is the prefix length. It states that the first 24 bits are the network prefix of the address (and the remaining 8 bits are available for specific host addresses)
CIDR notation can nicely express blocks of addresses
  An address block
  [128.195.0.0, 128.195.255.255]
  can be represented by an address prefix 128.195.0.0/16
  How many IP addresses are there in a /x address block?
    2 (32-x)

## Slide 46: IP Forwarding

## Slide 47: Delivery of an IP datagram
IP
View at the data link layer:
  Internetwork is a collection of LANs or point-to-point links or switched networks that are connected by routers

## Slide 48: Delivery of an IP datagram
IP
View at the IP layer:
  An IP network is a logical entity with a network number
  We represent an IP network as a “cloud”
  The IP delivery service takes the view of clouds, and ignores the data link layer view

## Slide 49: Delivery of IP datagrams
There are two distinct processes to delivering IP datagrams:
1. Forwarding (data plane): How to pass a packet from an input interface to the output interface?
2. Routing (control plane): How to find and setup the forwarding tables?
Ethernet analogy: spanning tree protocol
Forwarding must be done as fast as possible:
  On routers, is often done with support of hardware
  On PCs, is done in the kernel of the operating system
Routing is less time-critical
  Done in software

## Slide 50: Routing tables
Each router and each host keeps a routing table which tells the router where to forward an outgoing packet
Main columns:
    Destination address: where is the IP datagram going to?
    Next hop: how to send the IP datagram?
    Interface: what is the output port?
Next hop and interface column can often be summarized as one column
Routing tables are set so that datagrams get closer to the its destination
Destination | Next Hop | interface
10.1.0.0/24 10.1.2.0/24 10.2.1.0/24 10.3.1.0/24 20.1.0.0/16 20.2.1.0/28 | direct direct R4 direct R4 R4 | eth0 eth0 serial0 eth1 eth0 eth0
Routing table of a host or router
IP datagrams can be directly delivered (“direct”) or is sent to a router (“R4”)

## Slide 51: Delivery with routing tables
to: 20.2.1.2

## Slide 52: Processing of an IP datagram

## Slide 53: Processing of an IP datagram in
Processing of IP datagrams is very similar on an IP router and a host
Main difference: “IP forwarding” is enabled on router and disabled on host
IP forwarding enabled  if a datagram is received, but it is not for the local system, the datagram will be sent to a different system
IP forwarding disabled  if a datagram is received, but it is not for the local system, the datagram will be dropped

## Slide 54: Processing of an IP datagram at a router
IP header validation
Process options in IP header
  not required for lab2
Parsing the destination IP address
Routing table lookup
Decrement TTL
Perform fragmentation (if necessary)
  not required for Lab 2
Calculate checksum
Transmit to next hop
Send ICMP packet (if necessary)
Receive an IP datagram

## Slide 55: Forwarding table lookup
When a router or host needs to transmit an IP datagram, it performs a routing table lookup
Forwarding table lookup: Use the IP destination address as a key to search the routing table
Result of the lookup is the IP address of a next hop router, and/or the name of a network interface
Destination address | Next hop/ interface
network prefix or host IP address or loopback address or default route | IP address of next hop router or Name of a network interface

## Slide 56: Type of forwarding table entries
Network route
  Destination addresses is a network address (e.g., 10.0.2.0/24)
  Most entries are network routes
Host route
  Destination address is an interface address (e.g., 10.0.1.2/32)
  Used to specify a separate route for certain hosts
Default route
  Used when no network or host route matches
Loopback address
  Routing table for the loopback address (127.0.0.1)
  The next hop lists the loopback (lo0) interface as outgoing interface

## Slide 57: Forwarding table lookup algorithm
=
Longest Prefix Match: Search for the forwarding table entry that has the longest match with the prefix of the destination IP address
Search for a match on all 32 bits
Search for a match for 31 bits
…..
32. Search for a match on 0 bits
Host route, loopback entry  32-bit prefix match
Default route is represented as 0.0.0.0/0  0-bit prefix match
128.143.71.21
The longest prefix match for 128.143.71.21 is for 24 bits with entry 128.143.71.0/24
Datagram will be sent to R4
Destination address
Next hop
10.0.0.0/8
128.143.0.0/16
128.143.64.0/20
128.143.192.0/20
128.143.71.0/24
128.143.71.55/32
0.0.0.0/0 (default)
R1
R2
R3
R3
R4
R3
R5

## Slide 58: Advantages of longest prefix lookup
Scalable
  Multiple entries can be merged into one
  One entry can summarize multiple networks
    Default route: 0/0

## Slide 59: Today
Wrapping up switching technologies
  Review learning bridges
  Asynchronous Transfer Mode (ATM)
New topic: how to connect different types of networks
  E.g., how to connect an Ethernet and an ATM network

## Slide 60: Admin
Lab 1 is out, Due in two weeks
Midterm
  Thursday, March 6
  In class
  Closed notes, books, laptops, etc.
  One cheat sheet
  Covering up to lecture 13 (IP multicast)

## Slide 61: CS 356 Lab1 Reliable Transport

## Slide 62: Objective
A reliable data connection between two processes on top of UDP which is unreliable
  Handle Packet drop, reordering, corruption
  Provide flow control
                Sliding Window (Both sender and receiver)
                Two independent data links each connection:
Process A
Process B
Link 1
Link 2

## Slide 63: What can the program do
xwy@linux21$./reliable 6666 linux22:5555
[listening on UDP port 6666]
Hello!
On machine linux21, run:
On machine linux22, run:
xwy@linux22$./reliable 5555 linux21:6666
[listening on UDP port 5555]
Hello!

## Slide 64: Implementation
reliable.c: functions you need to fill in
rlib.c & rlib.h:
  the library supporting code
  Just need to know which functions you should call
reference: a solution program for reliable
tester: Use it to debug (-v option) and grade your program
xwy@linux22> ./tester ./reliable

## Slide 65: Data Flow
conn_input()
Sent out into network
Reliable
STDIN
Library Functions
STDOUT
Receive from network
conn_output()
Library Functions
Reliable
You cannot use printf() in your program, because it would be considered as data received from the sender. Use fprintf(stderr, “…”, …) instead

## Slide 66: reliable.c
reliable_state (also defined as rel_t)
  A data structure to maintain the connection state for one reliable connection
  Should include two sliding windows (one for sending and one for receiving)
  Add as much things as you need for the connection
rel_create(), rel_destroy(), rel_recvpkt(), rel_read(), rel_output(), rel_timer()
  Six functions you need to implement
  Refer to the lab1 tutorial for details

## Slide 67: Some Hints
The original code actually support two running mode: single connection mode and server/client mode. Only the first one is required
Only when two data links both terminated with EOF from STDIN (Ctrl+D in Linux) should the connection be destroyed. Remember to report EOF to conn_output.
Use htonl()/htons() to write a header and ntohl()/ntohs() to read a header.

## Slide 68: More Hints
Use while loop in the rel_read(). If conn_input() returns -1, handle the EOF packet and break from the loop. If conn_input() returns 0, simply break from the loop. If the sender’s window is full, break from the loop even if there is still more data from conn_input().
Call rel_read() to ask for more data after you received some ack packets and some slots in the sender’s window become vacant again.