## Slide 1: CS 356: Computer Network Architectures Lecture 12: Dynamic routing protocols: Link State Chapter 3.3.3
Xiaowei Yang
xwy@cs.duke.edu

## Slide 2: Today
Routing information protocol (RIP)
Link-state routing
  Algorithm
  Protocol: Open shortest path first (OSPF)

## Slide 3: Dynamic Routing
There are two parts related to IP packet handling:
  Forwarding (per-node operation): how to pass a packet from an input interface to the output interface of a router
  Routing (distributed algorithm): how to find and setup a route ?
    Implemented by dynamic routing protocols

## Slide 4: What distributed routing algorithms common routing protocols use
Routing information protocol (RIP) | Distance vector
Interior Gateway routing protocol (IGRP, cisco proprietary) | Distance vector
Open shortest path first (OSPF) | Link state
Intermediate System-to-Intermediate System (IS-IS) | Link state
Border gateway protocol (BGP) | Path vector
Routing protocol
Distributed algorithm

## Slide 5: Distance vector algorithm: initialization
Let Dx(y) be the estimate of least cost from x to y
Initialization:
  Each node x knows the cost to each neighbor: c(x,v). For each neighbor v of x, Dx(v) = c(x,v)
  Dx(y) to other nodes are initialized as infinity
Each node x maintains a distance vector (DV):
  Dx = [Dx(y): y ∈ N ]

## Slide 6: Distance vector algorithm: updates
Each node x sends its distance vector to its neighbors, either periodically, or triggered by a change in its DV
When a node x receives a new DV estimate from a neighbor v, it updates its own DV using the B-F equation:
  If c(x,v) + Dv(y) < Dx(y) then
    Dx(y) = c(x,v) + Dv(y)
    Sets the next hop to reach the destination y to the neighbor v
    Notify neighbors of the change
The estimate Dx(y) will converge to the actual least cost dx(y)

## Slide 7: RIP - Routing Information Protocol
A simple intradomain protocol
Straightforward implementation of Distance Vector Routing
Each router advertises its distance vector every 30 seconds (or whenever its routing table changes) to all of its neighbors
RIP always uses 1 as link metric
Maximum hop count is 15, with “16” equal to “”
Routes are timeout (set to 16) after 3 minutes if they are not updated

## Slide 8: RIP - History
Late 1960s : Distance Vector protocols were used in the ARPANET
Mid-1970s: XNS (Xerox Network system) routing protocol is the ancestor of RIP in IP (and Novell’s IPX RIP and Apple’s routing protocol)
1982 Release of routed for BSD Unix
1988 RIPv1 (RFC 1058) - classful routing
1993 RIPv2 (RFC 1388) - adds subnet masks with each route entry - allows classless routing
1998 Current version of RIPv2 (RFC 2453)

## Slide 9: RIPv1 Packet Format
One RIP message can have up to 25 route entries
1: request 2: response
2: for IP
Address of destination
Cost (measured in hops)
1: RIPv1

## Slide 10: RIPv2
RIPv2 is an extends RIPv1:
  Subnet masks are carried in the route information
  Authentication of routing messages
  Route information carries next-hop address
  Uses IP multicasting to send routing messages
Extensions of RIPv2 are carried in unused fields of RIPv1 messages

## Slide 11: RIPv2 Packet Format
One RIP message can have up to 25 route entries
1: request 2: response
2: for IP
Address of destination
Cost (measured in hops)
2: RIPv2
Notes: RFC 2453 says the only type is plain password.

## Slide 12: RIPv2 Packet Format
Used to provide a method of separating "internal" RIP routes (routes for networks within the RIP routing domain) from "external" RIP routes
Identifies a better next-hop address on the same subnet than the advertising router, if one exists (otherwise 0….0)
2: RIPv2
Subnet mask for IP address

## Slide 13: RIP Messages
This is the operation of RIP in routed. Dedicated port for RIP is UDP port 520.
Two types of messages:
  Request messages
    used to ask neighboring nodes for an update
  Response messages
    contains an update

## Slide 14: Routing with RIP
Initialization: Send a request packet (command = 1, address family=0..0) on all interfaces:
    RIPv1 uses broadcast if possible,
    RIPv2 uses multicast address 224.0.0.9, if possible
requesting routing tables from neighboring routers
Request received: Routers that receive above request send their entire routing table
Response received: Update the routing table
Regular routing updates: Every 30 seconds, send all or part of the routing tables to every neighbor in an response message
Triggered Updates: Whenever the metric for a route changes, send entire routing table.

## Slide 15: RIP Security
Issue: Sending bogus routing updates to a router
RIPv1: No protection
RIPv2: Simple authentication scheme
2: plaintext password

## Slide 16: RIP Problems
RIP takes a long time to stabilize
  Even for a small network, it takes several minutes until the routing tables have settled after a change
RIP has all the problems of distance vector algorithms, e.g., count-to-Infinity
        RIP uses split horizon to avoid count-to-infinity
The maximum path in RIP is 15 hops

## Slide 17: Link-state routing aims to address those problems

## Slide 18: Distance Vector vs. Link State Routing
With distance vector routing, each node has information only about the next hop to a destination
    Node A: to reach F go to B
    Node B: to reach F go to D
    Node D: to reach F go to E
    Node E: go directly to F
Distance vector routing makes poor routing decisions if directions are not completely correct (e.g., because a node is down).
  Count to infinity
If parts of the directions incorrect, the routing may be incorrect until the routing algorithms has re-converged.
A
B
C
D
E
F

## Slide 19: Distance Vector vs. Link State Routing
In link state routing, each node has a complete map of the topology
If a node fails, each node can calculate the new route
Challenge: All nodes need to have a consistent view of the network
A
B
C
D
E
F
A
B
C
D
E
F
A
B
C
D
E
F
A
B
C
D
E
F
A
B
C
D
E
F
A
B
C
D
E
F
A
B
C
D
E
F

## Slide 20: Link State Routing: Basic operations
  Each router establishes a relationship (“adjacency”) with its neighbors
  2. Each router generates a link state advertisement (LSA) which is reliably flooded to all routers
    ID of the node that creates the LSP
    List of neighbors and costs of the links
    A sequence number
    TTL
  3. Each router maintains a database of all received LSAs (topological database or link state database), which describes the network has a graph with weighted edges
  4. Each router uses its link state database to run a shortest path algorithm (Dijkstra’s algorithm) to produce the shortest path to each network

## Slide 21: Link state routing: graphical illustration
a
b
c
d
3
1
6
2
a
3
6
b
c
a
b
c
3
1
a
b
c
d
1
6
c
d
2
a’s view
b’s view
c’s view
d’s view
Collecting all pieces yield
a complete view of the network!

## Slide 22: Operation of a Link State Routing protocol
Received LSPs
IP Routing Table
Dijkstra’s
Algorithm
Link State Database
LSPs are flooded to other interfaces

## Slide 23: Reliable flooding
We’ve learned a flooding algorithm used by Ethernet switches
Question: why is it insufficient for link-state routing?
  Lost LSAs may result in inconsistent topologies at different routers
  Inconsistent topologies may lead to routing loops

## Slide 24: Reliable flooding
LSPs are transmitted reliably between adjacent routers
  ACK and retransmission
For a node x, if it receives an LSA sent by y
  Stores LSA(y) if it does not have a copy
  Otherwise, compares SeqNo. If newer, store; otherwise discard
  If a new LSA(y), floods LSA(y) to all neighbors except the incoming neighbor

## Slide 25: An example of reliable flooding

## Slide 26: When to flood an LSP
Triggered if a link’s state has changed
  Detecting failure
    Neighbors exchange hello messages
    If not receiving hello, assume dead
Periodic generating a new LSA
  Fault tolerance (what if LSA in memory is corrupted?

## Slide 27: Path computation
Dijkstra’s Shortest Path Algorithm for a Graph
Input: Graph (N,E) with N the set of nodes and E the set of edges
cvw link cost (cvw = ∞ if (v,w)  E, cvv = 0)
s source node.
Output: Dn cost of the least-cost path from node s to node n
M = {s};
for each n  M
Dn = csn;
while (M  all nodes) do
Find w  M for which Dw = min{Dj ; j  M};
Add w to M;
for each neighbor n of w and n  M
Dn = min[ Dn, Dw + cwn ];
Update route;
enddo
Notes: e start with M containing this node s and then initialize the table of costs (the C(n)s) to other nodes using the known costs to directly connected nodes. We then look for the node that is reachable at the lowest cost (w) and add it to M. Finally, we update the table of costs by considering the cost of reaching nodes through w. In the last line of the algorithm, we choose a new route to node n that goes through node w if the total cost of going from the source to w and then following the link from w to n is less than the old route we had to n. This procedure is repeated until all nodes are incorporated in M .

## Slide 28: Practical Implementation: forward search algorithm
More efficient: extracting min from a smaller set rather than the entire graph
Two lists: Tentative and Confirmed
Each entry: (destination, cost, nextHop)
Confirmed = {(s,0,s)}
Let Next = Confirmed.last
For each Nbr of Next
  Cost = myNext + Next  Nbr
    If Neighbor not in Confirmed or Tentative
      Add (Nbr, Cost, my.Nexthop(Next)) to Tentative
  If Nbr is in Tentative, and Cost is less than Nbr.Cost, update Nbr.Cost to Cost
If Tentative not empty, pick the entry with smallest cost in Tentative and move it to Confirmed, and return to Step 2
  Pick the smallest cost from a smaller list Tentative, rather than the rest of the graph

## Slide 29
Step | Confirmed | Tentative
1 | (D,0,-) | 
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 

## Slide 30
Step | Confirmed | Tentative
1 | (D,0,-) | 
2 | (D,0,-) | (B,11,B), (C,2,C)
3 | (D,0,-), (C,2,C) | (B,11,B)
4 | (D,0,-), (C,2,C) | (B,5,C) (A,12,C)
5 | (D,0,-), (C,2,C), (B,5,C) | (A,12,C)
6 | (D,0,-),(C,2,C),(B,5,C) | (A,10,C)
7 | (D,0,-),(C,2,C),(B,5,C), (A,10,C) | 

## Slide 31: OSPF
OSPF = Open Shortest Path First
  Open stands for open, non-proprietary
A link state routing protocol
The complexity of OSPF is significant
  RIP (RFC 2453 ~ 40 pages)
  OSPF (RFC 2328 ~ 250 pages)
History:
  1989: RFC 1131 OSPF Version 1
  1991: RFC1247 OSPF Version 2
  1994: RFC 1583 OSPF Version 2 (revised)
  1997: RFC 2178 OSPF Version 2 (revised)
  1998: RFC 2328 OSPF Version 2 (current version)

## Slide 32: Features of OSPF
Provides authentication of routing messages
  Similar to RIP 2
Allows hierarchical routing
  Divide a domain into sub-areas
Enables load balancing by allowing traffic to be split evenly across routes with equal cost

## Slide 33: OSPF Packet Format
Destination IP: neighbor’s IP address or 224.0.0.5 (ALLSPFRouters) or 224.0.0.6 (AllDRouters)
TTL: set to 1 (in most cases)
OSPF packets are not carried as UDP payload!
OSPF has its own IP protocol number: 89
Link state advertisement

## Slide 34: OSPF Common header
2: current version is OSPF V2
Message types:
1: Hello (tests reachability)
2: Database description
3: Link Status request
4: Link state update
5: Link state acknowledgement
ID of the Area from which the packet originated
Standard IP checksum taken over entire packet
0: no authentication
1: Cleartext password
2: MD5 checksum
(added to end packet)
Authentication passwd = 1: 64 cleartext password
Authentication passwd = 2: 0x0000 (16 bits)
KeyID (8 bits)
Length of MD5 checksum (8 bits) Nondecreasing sequence number (32 bits)
Prevents replay attacks
Notes: This field is the checksum of the complete contents of the
LSA, excepting the LS age field. The LS age field is
excepted so that an LSA's age can be incremented without
updating the checksum.
34

## Slide 35: OSPF LSA Format
LSAs
  Type 1: cost of links between routers
  Type 2: networks to which the router connects
  Others: hierarchical routing
LSA Header
Link 1
Link 2
Link State ID
link state sequence number
advertising router
Link Age
Link Type
checksum
length
Notes: 12.1.3. LS type The LS type field dictates the format and function of the LSA. LSAs of different types have different names (e.g., router-LSAs or network-LSAs). All LSA types defined by this memo, except the AS-external-LSAs (LS type = 5), are flooded throughout a single area only. AS-external-LSAs are flooded throughout the entire Autonomous System, excepting stub areas (see Section 3.6). Each separate LSA type is briefly described below in Table 15.
In addition, the Link Data field is specified for each link. This field gives 32 bits of extra information for the link. For links to transit networks, numbered point-to-point links and virtual links, this field specifies the IP interface address of the associated router interface (this is needed by the routing table calculation, see Section 16.1.1). For links to stub networks, this field specifies the stub network's IP address mask.
LS Type LSA description ________________________________________________ 1 These are the router-LSAs. They describe the collected states of the router's interfaces. For more information, consult Section 12.4.1. ________________________________________________ 2 These are the network-LSAs. They describe the set of routers attached to the network. For more information, consult Section 12.4.2. ________________________________________________ 3 or 4 These are the summary-LSAs. They describe inter-area routes, and enable the condensation of routing information at area borders. Originated by area border routers, the Type 3 summary-LSAs describe routes to networks while the Type 4 summary-LSAs describe routes to AS boundary routers. ________________________________________________ 5 These are the AS-external-LSAs. Originated by AS boundary routers, they describe routes to destinations external to the Autonomous System. A default route for the Autonomous System can also be described by an AS-external-LSA.

## Slide 36: Type 1 LSA
Link state ID and Advertising router are the same, 32-bit router ID
Link ID: router ID at the other end of the link
Link Data: identify parallel links
Metric: cost of the link
Type: types of the link e.g., point-to-point

## Slide 37: Open question
How to set link metrics?
Design choice 1: all to 1
Design choice 2: based on load
  Problems?
In practice: static

## Slide 38: Hierarchical OSPF

## Slide 39: Hierarchical OSPF
Two-level hierarchy: local area, backbone.
  Link-state advertisements only in area
  Each nodes has detailed area topology; only know direction (shortest path) to nets in other areas.
Area border routers: “summarize” distances to nets in own area, advertise to other Area Border routers.
Backbone routers: run OSPF routing limited to backbone.

## Slide 40: Scalability and Optimal Routing
A frequent tradeoff in network design
Hierarchy introduces information hiding
ABR

## Slide 41: OSPF summary
A link-state routing protocol
Each node has a map of the network and uses Dijkstra to compute shortest paths
Nodes use reliable flooding to keep an identical copy of the network map

## Slide 42: Summary
Routing information protocol (RIP)
Link-state routing
  Algorithm
  Protocol: Open shortest path first (OSPF)