## Slide 1: CS 356: Computer Network Architectures Lecture 19: Integrated Services and Differentiated Services
Xiaowei Yang
xwy@cs.duke.edu

## Slide 2: Overview
2
Why QoS?
  Architectural considerations
Approaches to QoS
  Fine-grained: Integrated services
    RSVP
  Coarse-grained:
    Differentiated services
Notes: Fine-grained: guarantees for each individual flow

## Slide 3: Components of Integrated Services
3
Service classes
  What does the network promise?
Service interface
  How does the application describe what it wants?
Establishing the guarantee
  How is the promise communicated to/from the network
  How is admission of new applications controlled?
Packet scheduling
  How does the network meet promises?

## Slide 4: 1. Service classes
4
  What kind of promises/services should network offer?
  Depends on the characteristics of the applications that will use the network ….

## Slide 5: Service classes
5
Guaranteed service
  For intolerant and rigid applications
  Fixed guarantee, network meets commitment as long as clients send at match traffic agreement
Controlled load service
  For tolerant and adaptive applications
  Emulate lightly loaded networks
Datagram/best effort service
  Networks do not introduce loss or delay unnecessarily
Notes:   Two components
    If conditions do not change, commit to current service
    If conditions change, take steps to deliver consistent performance (help apps minimize playback delay)
    Implicit assumption – network does not change much over time

## Slide 6: Components of Integrated Services
6
Type of commitment
  What does the network promise?
Service interface
  How does the application describe what it wants?
Establishing the guarantee
  How is the promise communicated to/from the network
  How is admission of new applications controlled?
Packet scheduling
  How does the network meet promises?

## Slide 7: Service interfaces
Flowspecs
  TSpec: a flow’s traffic characteristics
    Difficult: bandwidth varies
  RSpec: the service requested from the network
    Service dependent
      E.g. controlled load

## Slide 8: A Token Bucket Filter
8
Operation:
  If bucket fills, tokens are discarded
  Sending a packet of size P uses P tokens
  If bucket has P tokens, packet sent at max rate, else must wait for tokens to accumulate
Tokens enter bucket
at rate r
Bucket depth b: capacity of bucket

## Slide 9: Token Bucket Operations
9
Tokens
Packet
Overflow
Tokens
Tokens
Packet
Enough tokens 
packet goes through,
tokens removed
Not enough tokens  wait for tokens to accumulate

## Slide 10: Token Bucket Characteristics
10
In the long run, rate is limited to r
In the short run, a burst of size b can be sent
Amount of traffic entering at interval T is bounded by:
  Traffic = b + r*T
Information useful to admission algorithm

## Slide 11: Token Bucket Specs
11
BW
Time
1
2
1
2
3
Flow A
Flow B
Flow A: r = 1 MBps, B=1 byte
Flow B: r = 1 MBps, B=1MB

## Slide 12: TSpec
TokenBucketRate
TokenBucketSize
PeakRate
MinimumPolicedUnit
MaximumPacketSize

## Slide 13: Service Interfaces: RSpec
13
Guaranteed Traffic
  TokenRate and DelayVariation
  Or DelayVariation and Latency
Controlled load
  Type of service

## Slide 14: Components of Integrated Services
14
Type of commitment
  What does the network promise?
Service interface
  How does the application describe what it wants?
Establishing the guarantee
  How is the promise communicated to/from the network
  How is admission of new applications controlled?
Packet scheduling
  How does the network meet promises?

## Slide 15: RSVP Goals
15
Used on connectionless networks
  Robust
  Should not replicate routing functionality
  Should co-exist with route changes
Support for multicast
Modular design – should be generic “signaling” protocol
Approaches
  Receiver-oriented
  Soft-state
Notes:   Different receivers have different capabilities and want different QOS
  Changes in group membership should not be expensive
  Reservations should be aggregate – I.e. each receiver in group should not have to reserve
  Should be able to switch allocated resource to different senders

## Slide 16: RSVP Service Model
16
Make reservations for simplex data streams
Receiver decides whether to make reservation
Control msgs in IP datagrams (proto #46)
PATH/RESV sent periodically to refresh soft state
Notes: One pass:
  Failed requests return error messages - receiver must try again
  No e2e ack for success

## Slide 17: PATH Messages
17
PATH messages carry sender’s Tspec
  Token bucket parameters
Routers note the direction PATH messages arrived and set up reverse path to sender
Receivers send RESV messages that follow reverse path and setup reservations
If reservation cannot be made, user gets an error

## Slide 18: RESV Messages
18
Forwarded via reverse path of PATH
A receiver sends RESV messages
  TSpec from the sender
  Rspec

## Slide 19: Admission control
Router performs admission control and reserves resources
  If request rejected, send error message to receiver
  Guaranteed service: a yes/no based on available bandwidth
  Controlled load: heuristics
    If delay has not exceeded the bound last time after admitting a similar flow, let it in

## Slide 20: Soft State to Adapt to Routing Changes
20
Problems: Routing protocol makes routing changes
Solution:
  PATH and RESV messages sent periodically
  Non-refreshed state times out automatically
Ex: a link fails. How is a new reservation established?

## Slide 21: Merging multicast reservations
A requests a delay < 100ms
B requests a delay < 200ms

## Slide 22: Components of Integrated Services
22
Type of commitment
  What does the network promise?
Service interface
  How does the application describe what it wants?
Establishing the guarantee
  How is the promise communicated to/from the network
  How is admission of new applications controlled?
Packet scheduling
  How does the network meet promises?

## Slide 23: Packet classification and scheduling
Map a packet to a service class
  (src addr, dst addr, proto, src port, dst port)
Use scheduling algorithms to provide the service
  An implementation issue

## Slide 24: Scheduling for Guaranteed Traffic
24
Use WFQ at the routers
  Q: will DRR work?
Each flow is assigned to its individual queue
Parekh’s bound for worst case queuing delay = b/r
  b = bucket depth
  r = rate of arrival

## Slide 25: Controlled Load Service
25
Goals:
Isolation
  Isolates well-behaved from misbehaving sources
Sharing
  Mixing of different sources in a way beneficial to all
Possible Mechanisms:
WFQ
  Aggregate multiple flows into one WFQ

## Slide 26: Unified Scheduling
26
Scheduling: use WFQ in routers
Controlled Load
Class I
Controlled Load
Class II
Best Effort
Guaranteed Service
Guaranteed Service
Notes: Each guaranteed flow gets its own queue
All controlled load service flows and best effort aggregates in single separate queue
  Controlled load classes
    Worst case delay for classes separated by order of magnitude
    When high priority needs extra bandwidth – steals it from lower class
  Best effort traffic acts as lowest priority class

## Slide 27: Scalability
A lot of requests and state!
ISPs feel it is not the right service model for them!
Per-flow reservation/queue
  OC-48 link 2.5Gbps
  64Kbps audio stream
   39,000 flows
  Reservation and state needs to be stored in memory, and refreshed periodically
  Classify, police, and queue each flow

## Slide 28: Comments on RSVP
Not widely deployed as a commercial service
Used for other purposes
  Setting up MPLS tunnels etc.

## Slide 29: DiffServ

## Slide 30: Motivation of DiffServ
30
Analogy:
  Airline service, first class, coach, various restrictions on coach as a function of payment
Economics and assurances
  Pay more, and get better service
  Best-effort expected to make up bulk of traffic,
  Revenue from first class important to economic base
  Not motivated by real-time or maximizing social welfare
Notes: (will pay for more plentiful bandwidth overall)

## Slide 31: Basic Architecture
31
Agreements/service provided within a domain
  Service Level Agreement (SLA) with ISP
Edge routers do traffic conditioning
  Shaping, Policing, and Marking
Core routers
  Process packets based on packet marking and defined per hop behavior (PHB)
More scalable than IntServ
  No per flow state or signaling
Notes:   Edge routers: Perform per aggregate shaping and policing
  Mark packets with a small number of bits; each bit encoding represents a class or subclass

## Slide 32: DiffServ Architecture Example
AT&T
UNC
Duke
Shaping, policing, marking
Per-hop behavior

## Slide 33: Per-hop Behaviors (PHBs)
33
Define behavior of individual routers rather than end-to-end services; there may be many more services than behaviors
  No end-to-end guarantee
Multiple behaviors – need more than one bit in the header
Six bits from IP TOS field are taken for Diffserv code points (DSCP)

## Slide 34: Per-hop Behaviors (PHBs)
34
Two PHBs defined so far
Expedited forwarding aka premium service (type P)
  Possible service: providing a virtual wire
Assured forwarding (type A)
  Possible service: strong assurance for traffic within profile and allow source to exceed profile
Notes:   Admitted based on peak rate
  Unused premium goes to best effort
  Based on expected capacity usage profiles
  Traffic unlikely to be dropped if user maintains profile
  Out-of-profile traffic marked

## Slide 35: Expedited Forwarding PHB
35
  Goal: EF packets are forwarded with minimal delay and loss
Mechanisms:
  User sends within profile and network commits to delivery with requested profile
  Rate limiting of EF packets at edges only, using token bucket to shape transmission
  Priority or Weighted Fair Queuing

## Slide 36: Assured Forwarding PHB
36
Goal: good services for in-profile traffic
Mechanisms:
  User and network agree to some traffic profile
    How to define profiles is an open/policy issue
  Edges mark packets up to allowed rate as “in-profile” or low drop precedence
  Other packets are marked with one of two higher drop precedence values
  Random Early Detection in/out queues
Notes: A congested DS node tries to protect packets with a lower drop precedence value from being lost by preferably discarding packets with a higher drop precedence value
  Implemented using RED with In/Out bit

## Slide 37: DiffServ Architecture Example
AT&T
UNC
Duke
Shaping, policing, marking
Per-hop behavior
Edge
Core

## Slide 38: Edge Router Input Functionality
38
Packet
classifier
Traffic
Conditioner 1
Traffic
Conditioner N
Forwarding
engine
Arriving
packet
Best effort
Flow 1
Flow N
Classify packets based on packet header

## Slide 39: Traffic Conditioning
39
Wait for
token
Set EF bit
Packet
input
Packet
output
Test if
token
Set AF
“in” bit
token
No token
Packet
input
Packet
output
Drop on overflow

## Slide 40: Router Output Processing
Two queues: EF packets on higher priority queue
Lower priority queue implements RED “In or Out” scheme (RIO)
40
What DSCP?
If “in” set
incr in_cnt
High-priority Q
Low-priority Q
If “in” set
decr in_cnt
RIO queue
management
Packets out
EF
AF

## Slide 41: Router Output Processing
Two queues: EF packets on higher priority queue
Lower priority queue implements RED “In or Out” scheme (RIO)
41
What DSCP?
If “in” set
incr in_cnt
High-priority Q
Low-priority Q
If “in” set
decr in_cnt
RIO queue
management
Packets out
EF
AF

## Slide 42: Red with In or Out (RIO)
42
Similar to RED, but with two separate probability curves
Has two classes, “In” and “Out” (of profile)
“Out” class has lower Minthresh, so packets are dropped from this class first
  Based on queue length of all packets
As avg queue length increases, “in” packets are also dropped
  Based on queue length of only “in” packets

## Slide 43: RIO Drop Probabilities
43

## Slide 44: Pre-marking and traffic conditioning
44
first hop
router
internal
router
edge
router
CEO
edge
router
ISP
Company A
Unmarked
packet flow
Packets in premium
flows have bit set
Premium packet flow
restricted to R bytes/sec
Policing

## Slide 45: Edge Router Policing
45
Arriving
packet
Is packet
marked?
Token
available?
Token
available?
Clear “in” bit
Drop packet
Forwarding
engine
AF “in” set
EF set
Not marked
no
no

## Slide 46: Remarks on QoS
“Dead” at the Internet scale
Areas of success
  Enterprise networks
  Residential uplinks
  Datacenter networks

## Slide 47: Conclusion
QoS
  Why do we need it?
  Integrated Services
    + Fine techniques,
    - No economic model
    - Does not scale well
  Differentiated Services
    Motivated by business models
Looking forward
  DNS
  Applications