## Slide 1: CS 514 / ECE 558 Advanced Computer Networks
Transport Layer: TCP and QUIC
Slides courtesy of David Choffnes and Christo Wilson

## Slide 2: Transport Layer
Function:
  Demultiplexing of data streams
Optional functions (e.g., TCP):
  Creating long lived “connections”
  Reliable, in-order packet delivery
  Error detection
  Flow control and congestion control
Key challenges:
  Detecting and responding to congestion
  Balancing fairness against high utilization
Application
Transport
Network
Data Link
Physical

## Slide 3: End-to-end Argument
``The function in question can completely and correctly be implemented only with the knowledge and help of the application standing at the end points of the communication system. Therefore, providing that questioned function as a feature of the communication system itself is not possible.’’
End-to-end arguments in system design, J. H. Saltzer, D. P. Reed, and D. D. Clark, ACM Transactions on Computer Systems, Vol. 2, No. 4, Nov. 1984, pp. 277–288

## Slide 4: TCP Header Fields
Options
Destination Port
0
16
31
Sequence Number
Source Port
Acknowledgement Number
Advertised Window
Urgent Pointer
Flags
Checksum
4
HLen
Used to detect out of order, duplicate, and missing packets
Header length. Default length is 20 bytes, but may be longer with options.
Not used.
Used for flow control (protecting the receiver from overloading)
Used for connection establishment (SYN), acknowledgement (ACK), connection close (FIN), and errors (RST).

## Slide 5: Connection Setup
Why do we need connection setup?
  To establish state on both hosts
  Most important state: sequence numbers
    Count the number of bytes that have been sent
    Initial value chosen at random
    Why?
Important TCP flags (1 bit each)
  SYN – synchronization, used for connection setup
  ACK – acknowledge received data
  FIN – finish, used to tear down connection

## Slide 6: Three Way Handshake
Each side:
  Notifies the other of starting sequence number
  ACKs the other side’s starting sequence number (+1)
  Sequence # must increment on receiving a SYN
Client
Server
SYN <SeqC, 0>
SYN/ACK <SeqS, SeqC+1>
ACK <SeqC+1, SeqS+1>
Why
Sequence # +1?
Notes: Protocol designers decided that SYN and FIN flags would occupy one byte each in the sequence space (RFC 793, 1981)

## Slide 7: Sequence Number Space
TCP uses a byte stream abstraction
  Initial, random values selected during setup
  Each byte in each stream is numbered
  32-bit value, wraps around
Byte stream broken down into segments (packets)
  Size limited by the Maximum Segment Size (MSS, typically 1460 bytes)
  Set to limit fragmentation
Each segment has a sequence number
Segment 8
Segment 9
Segment 10
13450
14950
16050
17550

## Slide 8: Bidirectional Communication
Each side of the connection can send and receive
  Different sequence numbers for each direction
Client
Server
Data (1460 bytes)
Data/ACK (730 bytes)
Data/ACK (1460 bytes)
Seq.
Ack.
Seq.
Ack.
1
23
23
1461
1461
753
753
2921
Data and ACK in the same packet
23
1

## Slide 9: Flow Control
Problem: how many packets should a sender transmit?
  Too many packets may overwhelm the receiver
  Size of the receiver's buffers may change over time
Solution: sliding window
  Receiver tells the sender how big their buffer is
  Called the advertised window
  For window size n, sender may transmit n bytes without receiving an ACK
  After each ACK, the window slides forward
Advertised window may go to zero!

## Slide 10: Flow Control: View from the Sender Side
Sequence Number
Src. Port
Acknowledgement Number
Adv. Window
Urgent Pointer
Flags
Checksum
HL
Packet Sent
Dest. Port
Src. Port
Acknowledgement Number
Adv. Window
Urgent Pointer
Flags
Checksum
HL
Packet Received
Dest. Port
Sequence Number
ACKed
Sent
To Be Sent
Outside Window
Window
sock.send()
Must be buffered until ACKed
Buffer of Bytes to Send
Notes: Each side acts and sender and receiver
Every message contains sequence number, even if payload length is zero
Every message contains acknowledgements, even if no data was received
Every message advertises the window size

## Slide 11: What Should the Receiver ACK?
ACK every packet that extends contiguous received bytes in sequence space order
Use cumulative ACK, where an ACK for sequence n implies ACKS for all k < n
Use negative ACKs (NACKs), indicating which packet did not arrive
  not used by TCP
Use selective ACKs (SACKs), indicating those that did arrive, even if not in order
  SACK is an actual TCP extension, SACK-permitted options fields in header

## Slide 12: Error Detection
Checksum detects (some) packet corruption
  Computed over portion of IP header, TCP header, and data
Sequence numbers catch sequence problems
  Duplicates are ignored
  Out-of-order packets are reordered or dropped
  Missing sequence numbers indicate lost packets
Lost segments detected by sender
  Use timeout to detect missing ACKs
  Need to estimate RTT to calibrate the timeout
  Sender must keep copies of all data until ACK

## Slide 13: Retransmission Time Outs (RTO)
Problem: time-out is linked to round trip time
Initial Send
ACK
Retry
RTO
Initial Send
ACK
Retry
RTO
Timeout is too short
What about if timeout is too long?

## Slide 14: Round Trip Time Estimation
Original TCP round-trip estimator
  RTT estimated as a moving average
  new_rtt = α (old_rtt) + (1 – α)(new_sample)
  Recommended α: 0.8-0.9 (0.875 for most TCPs)
RTO = 2 * new_rtt (i.e. TCP is conservative)
Data
ACK
RTT Sample

## Slide 15: What is Congestion?
Load on the network is higher than capacity
  Capacity is not uniform across networks
    Modem vs. Cellular vs. Cable vs. Fiber Optics
  There are multiple flows competing for bandwidth
    Residential cable modem vs. corporate datacenter
  Load is not uniform over time
    10pm, Sunday night = BitTorrent Game of Thrones

## Slide 16: Why is Congestion Bad?
Results in packet loss
  Routers have finite buffers, packets may be dropped
Practical consequences
  Router queues build up, delay increases
  Wasted bandwidth from retransmissions
  Low network goodput

## Slide 17: The Danger of Increasing Load
Knee – point after which
  Throughput increases very slowly
  Delay increases quickly
In an M/M/1 queue
  Delay = 1/(1 – utilization)
Cliff – point after which
  Throughput  0
  Delay  ∞
Congestion Collapse
Load
Load
Goodput
Delay
Knee
Cliff
Ideal point

## Slide 18: Cong. Control vs. Cong. Avoidance
Congestion Collapse
Goodput
Knee
Cliff
Load
Congestion Avoidance:
Stay left of the knee
Congestion Control:
Stay left of the cliff

## Slide 19: Advertised Window, Revisited
Does TCP’s advertised window solve congestion?
NO
The advertised window only protects the receiver
A sufficiently fast receiver can max the advertised window (i.e. 216 bytes)
  What if the network is slower than the receiver?
  What if there are other concurrent flows?
Key points
  Window size determines send rate
  Window must be adjusted to prevent congestion collapse

## Slide 20: Goals of Congestion Control
Adjusting to the bottleneck bandwidth
Adjusting to variations in bandwidth
Sharing bandwidth between flows
Maximizing throughput

## Slide 21: General Approaches
Do nothing, send packets indiscriminately
  Many packets will drop, totally unpredictable performance
  May lead to congestion collapse
Reservations
  Pre-arrange bandwidth allocations for flows
  Requires negotiation before sending packets
  Must be supported by the network
Dynamic adjustment
  Use probes to estimate level of congestion
  Speed up when congestion is low
  Slow down when congestion increases
  Messy dynamics, requires distributed coordination

## Slide 22: TCP Congestion Control
Introduce a congestion window (cwnd) at the sender
  Congestion control is a sender-side problem
  Controls the number of unACKed packets
  Separate variable, but bounded by the receiver’s advertised window
Sending rate is ~ congestion window/RTT
  Why is the sending rate (inversely) proportional to RTT?
  Recall that TCP is ACK-clocked
Idea: vary the window size to control the send rate

## Slide 23: Two Basic Components
Detect congestion
  Packet dropping is most reliable signal
    Delay-based methods are hard and risky
  How do you detect packet drops? ACKs
    Timeout after not receiving an ACK
    Several duplicate ACKs in a row (starting in TCP Reno)
Rate adjustment algorithm
  Modify cwnd
  Probe for bandwidth
  Respond to congestion
Except on wireless networks

## Slide 24: Rate Adjustment
Recall: TCP is ACK clocked
  Congestion = delay = long wait between ACKs
  No congestion = low delay = ACKs arrive quickly
Basic algorithm
  Upon receipt of ACK: increase cwnd
    Data was delivered, perhaps we can send faster
    cwnd growth is proportional to RTT
  On loss: decrease cwnd
    Data is being lost, there must be congestion
Question: what increase/decrease functions to use?

## Slide 25: Utilization and Fairness
Flow 1 Throughput
Flow 2 Throughput
Max throughput for flow 2
Zero throughput for flow 1
Max throughput for flow 1
Zero throughput for flow 2
Less than full utilization
More than full utilization (congestion)
Ideal point
Max efficiency
Perfect fairness
Equal throughput
(fairness)

## Slide 26: Additive Increase, Multiplicative Decrease
Converges to stable and fair cycle
Symmetric around y=x
Flow 1 Throughput
Flow 2 Throughput

## Slide 27: Implementing Congestion Control
Maintains three variables:
  cwnd: congestion window
  adv_wnd: receiver advertised window
  ssthresh: slow start threshold (used to update cwnd)
For sending, use: wnd = min(cwnd, adv_wnd)
Two phases of congestion control
  Slow start (cwnd < ssthresh)
    Probe for bottleneck bandwidth
  Congestion avoidance (cwnd >= ssthresh)
    AIMD

## Slide 28: Slow Start
Goal: reach knee quickly
Upon starting (or restarting) a connection
  cwnd =1
  ssthresh = adv_wnd
  Each time a segment is ACKed, cwnd++
Continues until…
  ssthresh is reached
  Or a packet is lost
Slow Start is not actually slow
  cwnd increases exponentially
Load
Goodput
Knee
Cliff

## Slide 29: Slow Start Example
1
2
3
4
5
6
7
cwnd = 1
cwnd = 2
cwnd = 4
cwnd = 8
cwnd grows rapidly
Slows down when…
  cwnd >= ssthresh
  Or a packet drops

## Slide 30: Congestion Avoidance
AIMD mode
ssthresh is lower-bound guess about location of the knee
If cwnd >= ssthresh then each time a segment is ACKed cwnd += 1/cwnd
So cwnd is increased by one only if all segments have been acknowledged

## Slide 31: Congestion Avoidance Example
Round Trip Times
cwnd (in segments)
Slow Start
cwnd >= ssthresh
cwnd = 1
cwnd = 2
cwnd = 4
cwnd = 8
cwnd = 9
ssthresh = 8

## Slide 32: TCP Pseudocode
Initially: cwnd = 1; ssthresh = adv_wnd;
New ack received: if (cwnd < ssthresh) /* Slow Start*/ cwnd = cwnd + 1; else /* Congestion Avoidance */ cwnd = cwnd + 1/cwnd;
Timeout: /* Multiplicative decrease */ ssthresh = cwnd/2; cwnd = 1;

## Slide 33: The Big Picture
Time
cwnd
Timeout
Slow Start
Congestion
Avoidance
ssthresh

## Slide 34: The Evolution of TCP
Thus far, we have discussed TCP Tahoe
  Original version of TCP
However, TCP was invented in 1974!
  Today, there are many variants of TCP
Early, popular variant: TCP Reno
  Tahoe features, plus…
  Fast retransmit
  Fast recovery

## Slide 35: TCP Reno: Fast Retransmit
Problem: in Tahoe, if segment is lost, there is a long wait until the RTO
Reno: retransmit after 3 duplicate ACKs
1
2
3
4
5
6
7
cwnd = 1
cwnd = 2
cwnd = 4
1
2
3
3
3
3
3 Duplicate ACKs

## Slide 36: TCP Reno: Fast Recovery
Initially: cwnd = 1; ssthresh = adv_wnd;
slow_start = TRUE;
New ack received: if (slow_start) cwnd = cwnd + 1;
if (cwnd < ssthresh)
slow_start = FALSE; else /* Congestion Avoidance */ cwnd = cwnd + 1/cwnd;
3 duplicate acks: cwnd = cwnd/2;
Timeout:
/* Multiplicative decrease */
cwnd = 1; ssthresh = cwnd/2;
slow_start = TRUE;
After a fast-retransmit set cwnd to cwnd/2, stay in Congestion Avoidance
  i.e. don’t reset cwnd to 1
  Avoid unnecessary return to slow start
  Prevents expensive timeouts
But when RTO expires still do cwnd = 1
  Return to slow start, same as Tahoe
  Indicates packets aren’t being delivered at all
  i.e., congestion must be really bad

## Slide 37: Fast Retransmit and Fast Recovery
At steady state, cwnd oscillates around the optimal window size
TCP always forces packet drops
Time
cwnd
Timeout
Slow Start
Congestion Avoidance
Fast Retransmit/Recovery
ssthresh
Timeout

## Slide 38: Many TCP Variants…
Tahoe: the original
  Slow start with AIMD
  Dynamic RTO based on RTT estimate
Reno: fast retransmit and fast recovery
NewReno: improved fast retransmit
  Each duplicate ACK triggers a retransmission
  Problem: >3 out-of-order packets causes pathological retransmissions
Vegas: delay-based congestion avoidance
And many, many, many more…

## Slide 39: TCP in the Real World
What are popular variants today?
  Key problem: TCP performs poorly on high bandwidth-delay product networks (like the modern Internet)
  Compound TCP (Windows)
    Based on Reno
    Uses two congestion windows: delay based and loss based
    Thus, it uses a compound congestion controller
  TCP CUBIC (Linux)
    Enhancement of BIC (Binary Increase Congestion Control)
    Window size controlled by cubic function
    Parameterized by the time T since the last dropped packet
  TCP BBR (Google)
  QUIC [Not really TCP]

## Slide 40: High Bandwidth-Delay Product
Key Problem: TCP performs poorly when
  The capacity of the network (bandwidth) is large
  The delay (RTT) of the network is large
  bandwidth * delay is large
    b * d = maximum amount of in-flight data in the network
    a.k.a. the bandwidth-delay product
Why does TCP perform poorly?
  Slow start and additive increase are slow to converge when bandwidth is large
  TCP is ACK clocked
    i.e. TCP can only react as quickly as ACKs are received
    Large RTT  ACKs are delayed  TCP is slow to react

## Slide 41: TCP CUBIC Implementation
Default TCP implementation in Linux
Replace AIMD with cubic function
  C  a constant scaling factor
  β  a constant fraction for multiplicative decrease
  T  time since last packet drop
  cwndmax  cwnd when last packet dropped

## Slide 42: TCP CUBIC Example
Less wasted bandwidth due to fast ramp up
Stable region and slow acceleration help maintain fairness
  Fast ramp up is more aggressive than additive increase
  To be fair to Tahoe/Reno, CUBIC needs to be less aggressive
Time
cwnd
Timeout
Slow Start
CUBIC Function
cwndmax
Fast ramp up
Stable
Region
Slowly accelerate to probe for bandwidth

## Slide 43: Simulations of CUBIC Flows
CUBIC
CUBIC
Reno
Reno

## Slide 44: Deploying TCP Variants
TCP assumes all flows employ TCP-like congestion control
  TCP-friendly or TCP-compatible
  Violated by UDP :(
If new congestion control algorithms are developed, they must be TCP-friendly
Be wary of unforeseen interactions
  Variants work well with others like themselves
  Different variants competing for resources may trigger unfair, pathological behavior

## Slide 45: Initial Window Size
What should be the initial value of cwnd?
  Too small – flows take longer to leave slow start
  Too big – new flows create burst of traffic that may congest networks
Subject of ongoing debate
  E.g. Linux kernel officially adopted cwnd = 10 in 2011
What sizes are in use today?
Jan Rüth, Christian Bormann, Oliver Hohlfeld. Large-scale Scanning of TCP’s Initial Window. IMC 2017.

## Slide 46: SACK: Selective Acknowledgment
Problem: duplicate ACKs only tell us about 1 missing packet
  Multiple rounds of dup ACKs needed to fill all holes
Solution: selective ACK
  Include received, out-of-order sequence numbers in TCP header
  Explicitly tells the sender about holes in the sequence
8
9
10
11
4
4
5
6
7
4
4
4
4

## Slide 47: Issues with TCP
Most Internet traffic is TCP
However, many issues with the protocol
  Lack of fairness
  Synchronization of flows
  Poor performance with small flows
  Really poor performance on wireless networks
  Susceptibility to denial of service

## Slide 48: Synchronization of Flows
Ideal bandwidth sharing
cwnd
cwnd
cwnd
Oscillating, but high overall utilization
In reality, flows synchronize
One flow causes all flows to drop packets
Periodic lulls of low utilization

## Slide 49: Small Flows
Problem: TCP is biased against short flows
  1 RTT wasted for connection setup (SYN, SYN/ACK)
  cwnd always starts at a low number (10 as of ~2017)
Vast majority of Internet traffic is short flows
  Mostly HTTP transfers, <100KB
  Most TCP flows never leave slow start!
Proposed solutions
  Increase initial cwnd to a larger value, e.g., 64
  TCP Fast Open: use cryptographic hashes to identify receivers, eliminate the need for three-way handshake

## Slide 50: Wireless Networks
Problem: Tahoe and Reno assume loss = congestion
  True on the WAN, bit errors are very rare
  False on wireless, interference is very common
TCP throughput ~ 1/sqrt(drop rate)
  Even a few interference drops can kill performance
Possible solutions:
  Break layering, push data link info up to TCP
  Use delay-based congestion detection (TCP Vegas)
  Explicit congestion notification (ECN)
    Routers mark the 1-bit ECN field in the TCP header to indicate congestion

## Slide 51: Denial of Service
Problem: TCP connections require state
  Initial SYN allocates resources on the server
  State must persist for several minutes (RTO)
SYN flood: send enough SYNs to a server to allocate all memory/meltdown the kernel
Solution: SYN cookies
  Idea: don’t store initial state on the server
  Securely insert state into the sequence number in the SYN/ACK packet
  Client will reflect the state back to the server

## Slide 52: SYN Cookies
Did the client really send me a SYN recently?
  Timestamp: freshness check
  Cryptographic hash: prevents spoofed packets
Maximum segment size (MSS)
  Usually stated by the client during initial SYN
  Server should store this value…
  Reflect the client’s value back through them
Sequence Number
Timestamp
31
0
5
MSS
8
Crypto Hash of Client IP & Port

## Slide 53: SYN Cookies in Practice
Advantages
  Effective at mitigating SYN floods
  Compatible with all TCP versions
  Only need to modify the server
  No need for client support
Disadvantages
  MSS limited to 3 bits, may be smaller than clients actual MSS
  Server forgets all other TCP options included with the client’s SYN
    SACK support, window scaling, etc.

## Slide 54: TCP BBR
Motivation: Loss does not always imply congestion
Key idea: Model the bottleneck bandwidth rate using two properties
  Bottleneck bandwidth (btlBw)
  Propagation RTT (RTprop)
Send data using pacing so that one BDP of data is in flight at a time
  BDP = btlBw x Rtprop
Send rate limited by cwnd or pacing_rate (pacing_gain × BtlBw)
  Cwnd capped to 2 x BDP (to overcome delays in received acks)

## Slide 55: TCP BBR
BBR constantly measures BtlBw and Rtprop
Measuring BtlBw
  Finds maximum observed delivery rate over past 10 RTTs
  Periodically increases send rate to 1.25 x BtlBw to search for more bandwidth
Measuring Rtprop
  Finds min RTT over past 10 seconds based on ACKs
  Problem: BBR may induce queueing delays by sending too fast
  Solution: Periodically “drain” queues by sending at 25% less than BtlBw

## Slide 56: TCP BBR problems
Assumes delay increases correspond to congestion
  Does not work for short queues, and leads to incorrect BtlBw estimates
Fairness

## Slide 57: QUIC
Quick UDP Internet Connections
  Deployed by Google in 2013
  Now an Internet standard (part of HTTP/3)
  Provides reliable in-order byte streams, but using UDP
Motivation
  Experimenting with TCP is difficult to do quickly at scale (OS changes)
  Privacy/integrity violations are critical, so encrypt everything
QUIC is intended to replace TCP, TLS, and HTTP/2

## Slide 58: QUIC Features
“0-RTT” connection establishment
  Allows resumption of connections if client/server have communicated before
  No expensive 3-way handshake or TLS connection setup
Reduced “head of line” blocking
  Packet loss impacting one HTTP/2 stream does not affect others in the same connection
Improved congestion control
  Solves ACK ambiguity (lost packets vs retransmission vs out of order delivery)
  More precise timing information for RTT estimates
  Packet pacing to avoid bursty losses
  Window no longer pinned to last unACKed packet
  Pluggable CC algorithms (Cubic, BBR)
  Much, much more

## Slide 59: QUIC Problems
Fairness
(5 Mbps link, RTT=36ms, buffer = 30KB)
QUIC gets same bandwidth regardless of number of competing flows