## Slide 1: Engineering a Content Delivery Network
Bruce Maggs

## Slide 2: What does a CDN do?
DNS resolution
Delivery of static content (images, video, software)
Full-site (secure) web-site delivery
Delivery of live video
Defense against denial of service attacks

## Slide 3: The Akamai Platform and Services
Daily Statistics:
30+ Tbps traffic served
600+ million IPv4 addresses seen
3+ trillion requests served
260+ terabytes compressed logs
    Delivering Content for 130,000+ Domains
    All top 20 global ecommerce sites
    All top 30 media & entertainment companies
    16 of the top 20 global banks
    All major anti-virus software vendors
240,000+ Servers
1,700+ Networks
3,300+ Physical Locations
750+ Cities
130+ Countries
    A Global Platform:

## Slide 4: Benefits
Improved page load times
On demand scalability
Resistance to large-scale attacks

## Slide 5: Impact of PLT on conversion on e-commerce Web sites
Source: Akamai, State of Online Retail Performance, 2017 Holiday Perspective

## Slide 7: Largest DDOS Attacks by Year
Gbps
Krebs
GitHub
Chart: 
| 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
 | 11 | 18 | 22 | 39 | 48 | 68 | 79 | 82 | 190 | 321 | 309 | 623 | 109 | 1350

## Slide 8
Origin Server
End User
1
10
100
10000
Origin Traffic
1000
Akamai Traffic
1
10
100
10000
1000
Akamai Kona Site Defender

## Slide 9: Design Themes
Redundancy
Self-assessment
Fail-over at multiple levels
Robust algorithms

## Slide 10: Embedded Image Delivery
<html>
<head>
<title>Welcome to xyz.com!</title>
</head>
<body>
<img src=“
<img src=“
<h1>Welcome to our Web site!</h1>
<a href=“page2.html”>Click here to enter</a>
</body>
</html>
http://www.xyz.com/logos/logo.gif”>
http://www.xyz.com/jpgs/background.jpg”>
Embedded URLs are Converted to ARLs
ak
Notes: Very simple process.

## Slide 11: Akamai DNS Resolution
End User
Akamai High-Level DNS Servers
10
g.akamai.net
1
Browser’s Cache
OS
2
Local Name Server
3
xyz.com’s nameserver
6
ak.xyz.com
7
a212.g.akamai.net
9
15.15.125.6
16
15
11
20.20.123.55
Akamai Low-Level DNS Servers
12
a212.g.akamai.net
30.30.123.5
13
14
4
xyz.com
.com .net
Root (Verisign)
10.10.123.5
5
akamai.net
8
select cluster
select servers within cluster
Notes: One of many ways—don’t have to do cname but it is easy. Note that usually address is already in local name server and you don’t do all these steps.

## Slide 12: Live Streaming Architecture
Regions
1 2 3 4
1 2 3 4
x
1 2 3 4
X X X X
1 2 3 4
x
Satellite
Downlink
Entry Point
Satellite
Uplink
Top-level reflectors
Encoding
1 2 3 4
X

## Slide 13: Failures
Hardware
Network
Software
Configuration
Misperceptions
Attacks

## Slide 14: Akamai Cluster
Servers pool resources
RAM
Disk
Throughput

## Slide 16: View of Clusters
hardware
failure
buddy
suspended
suspended
datacenter
odd man
out

## Slide 17: Network Failures
E.g., congestion at public and private peering points, misconfigured routers, inaccessible networks, etc., etc., etc.

## Slide 18: Core Points
Core point X is the first router at which all paths to nameservers 1, 2, 3, and 4 intersect.
X can be viewed as the straddling the core and the edge of the network.
X
1
2
3
4

## Slide 19: Core Points
500,000 nameservers
reduced to
90,000 core points
7,000 account for 95% end-user load

## Slide 20: Engineering Methodology
C programming language (gcc).
Reliance on open-source code.
Large distributed testing systems.
Burn-in on “invisible” system.
Staged rollout to production.
Backwards compatibility.