## Slide 1: Software-defined Networking (SDN)
Slides originally by Anja Feldmann and Bala Chandrasekaran

## Slide 2: Network Switches and Routers (2007)
Million of lines of source code
Specified by 5400 RFCs
500M gates
10Gbytes RAM
Power Hungry
Many complex functions baked into the infrastructure
Learning Bridge, Spanning Tree Protocol, OSPF, BGP, MPLS, multicast,
NAT, firewalls, differentiated services, traffic engineering, …
An industry with a “mainframe-mentality”
Specialized Packet Forwarding Hardware
Operating
System
App
App
App
Routing, management, mobility management, access control, VPNs, …
Notes: 2

## Slide 3: Disadvantages of the Monolithic Approach
Closed equipment
  Software bundled with hardware
  Vendor-specific interfaces
Over specified
  Based on many “standards”
Few people can innovate
  Equipment vendors write the code
  Introducing new standards is very slow
Operating a network is expensive
  More than half the cost of a network
  Yet, operator error causes most outages
Buggy software in the equipment
  Routers with 20+ million lines of code
  Cascading failures, vulnerabilities, etc.
Notes: 3

## Slide 4: Traditional Networks: Data Plane
Packet streaming
  Forward, filter, buffer, mark,
  rate-limit, and measure packets
Fast but stupid
Responsible for forwarding packets
Notes: Maybe this is a better picture… though need some details of what happens in each plane… like in next slides… or, have both?

## Slide 5: Traditional Networks: Control Plane
  Track topology changes, compute routes, install forwarding rules
Distributed algorithms
(e.g., OSPF, BGP)
Slow but smart
Responsible for building routing tables
Notes: Maybe this is a better picture… though need some details of what happens in each plane… like in next slides… or, have both?

## Slide 6: Traditional Networks: Management Plane
  Collect measurements and configure the equipment
Management plane:
Human time scale
Slow but Really Smart
Notes: Maybe this is a better picture… though need some details of what happens in each plane… like in next slides… or, have both?

## Slide 7: Software-defined networking (SDN)
Simple and elegant idea:
Decoupling of control and data planes
Provide an open standard API

## Slide 8: Why? A look at network elements
Classical Switch:
Cisco 3548XL
A closed box
Control Hardware:
Embedded PC
Dataplane:
Interfaces, TCAM, Switch fabric
Control software
(Spanning Tree Protocol,
VLAN trunking protocol, etc. )

## Slide 9: Why? A look at network elements?
Operator says:
But I need a 3rd SPAN port!
Cisco's answer:
Buy one of these!

## Slide 10: Software Defined Networking (SDN)
API to the data plane
(e.g., OpenFlow)
Logically-centralized controller
Switches
Slow but Smart
Fast but
Dumb

## Slide 11: OpenFlow
SDN standard managed by the Open Network Foundation
Version 1.1 released in 2011
Supported by major switch vendors
Canonical example of SDN, but not widely used now
Scalability problems

## Slide 12: Controller: Network OS
[http://www.cs.princeton.edu/courses/archive/fall13/cos597E/docs/03API.pdf]

## Slide 13: Controller: Network OS
[http://www.cs.princeton.edu/courses/archive/fall13/cos597E/docs/03API.pdf]
Something happened …
Event
Here’s what you do …
Command
The controller or the application can generate the command.

## Slide 14: Controller: Events
OFPacketIn
  When first packet of a flow (with no matching rule in the flow table) arrives at an OF switch
  Attributes: Details to help the controller/application decide
    Switch ID, incoming port, headers, …

## Slide 15: Controller: Output/Command
OFPacketOut
  Instruction for the switch on what to do with the packet
    What to do? Forward, Drop
  Attributes: Details to help the switch carry out the action
    Action, buffer ID, …

## Slide 16: Controller: Network OS
src. MAC
dst. MAC
src. IP
dst. IP
src. port
dst. port
…
…
…
…
…
…
…
…
…
…
…
…
Flow Table
action
…
…
[http://www.cs.princeton.edu/courses/archive/fall13/cos597E/docs/03API.pdf]
OpenFlow v1.0
OFPacketOut
Command
OFPacketIn
Event
Inbound packet
Inbound packet
Inbound packet
Inbound packet

## Slide 17: Controller: Application example
OFPacketIn
    Switch ID: A, incoming port: 1, headers, …
OFPacketOut
    Switch ID: A, outgoing port: *, headers, …
Application?
  Hub

## Slide 18: SDNApplication: It can’t be that simple …
Well, here’s an example implementation
  # Create packet out message
  msg = of.ofp_packet_out()
  # Use the incoming packet as the data for the packet out
  msg.buffer_id = event.ofp.buffer_id
  # Set the in_port so that the switch knows
  msg.in_port = packet_in.in_port
  # Add an action to send to the specified port
  msg.match = of.ofp_match.from_packet(packet)
  action = of.ofp_action_output(port = of.OFPP_FLOOD)
  msg.actions.append(action)
  # Send message to switch
  self.connection.send(msg)

## Slide 19: Controller: Flow rules
Flow rules
  Rather than react to every packet from the switch, can install a rule that matches on certain packet headers
  Flow rules are installed by the controller and maintained in the flow table
    Flow rules are generated by applications (either bundled with the controller or running on top of the controller)

## Slide 20: Controller: More commands
OFFlowAdd
  Add a new rule that matches on certain headers (or attributes)
    e.g., all packets from src IP 1.2.3.4 and destined for 4.3.2.1 (regardless of other attributes) should be dropped (Think firewall!)
OFFlowMod
  Modify an existing rule in the switch
    e.g., Change the above rule to not drop such packets
OFStatisticsRequest
  Instructs Switch to reply with an OFStatisticsResponse containing some statistics on traffic received by this switch
  How? Switches also have counters/meters to gather metrics!

## Slide 21: Controller: More events
OFFlowRemoved
  Tells a controller that a flow rule was removed
  Flow rules can have (hard/soft) timeouts!
OFStatisticsResponse
  Statistics on traffic observed by the switch (could be useful for traffic engineering)

## Slide 22: SDN Controller: Event-driven paradigm
Switch generates events and sends them to controller
Application(s) responds to the events
  Controller has (or interacts with) one or more applications
  Application subscribes to (a subset of) events
  When application receives an event, it responds with an output (command)
  Controller sends this command to the switch

## Slide 23: SDN Controllers
Many exist!
  NOX (C++)
  POX (Python)
  Floodlight (Java)
  OpenDaylight (Java)
  Onix
  ONOS
  Pyretic
Different Implementations offer different services, applications, benefits, …

## Slide 24: SDN Controllers: Applications
Controllers may come bundled with one or more applications
  Floodlight, for instance, comes bundled with Hub, Switch, …
We can also deploy custom applications with the controller …
  A traffic engineering application that performs “smart” routing by gathering details about traffic conditions in the network (through OFStatisticsRequest)
  No need to reinvent the wheel
    There are SDN AppStores

## Slide 25: SDN Applications
Different applications can install rules that perform different actions for different matches
Flow Table
src. MAC
dst. MAC
src. IP
dst. IP
src. port
dst. port
action
…
…
…
…
…
…
…
…
…
…
…
…
…
…

## Slide 26: SDN Applications
Different applications can install rules that perform different actions for different matches
Flow Table
src. MAC
dst. MAC
src. IP
dst. IP
src. port
dst. port
action
*
H
…
…
…
…
port 8
…
…
X
Y
…
80
port 2
…
…
X
Y
*
443
port 4
…
…
X
Y
*
22
drop
Switching
Routing
Firewall

## Slide 27: SND Applications
Measurement
Traffic engineering
Security
Virtualization
E.g., see https://opennetworking.org/sdn-resources/sdn-reading-list/sdn-applications/

## Slide 28: Flow Table Entries
Rule
Action
Stats
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
+ mask
Packet + byte counters
Forward packet to port(s)
Encapsulate and forward to controller
Drop packet
Send to normal processing pipeline
…

## Slide 29: Topology Discovery
OpenFlow Discover Protocol (OFDP)
Controller sends link-layer discovery protocol (LLDP) message to switch at fixed intervals (e.g., 10s)
LLDP message forwarded to neighbor
Neighbor returns LLDP message to controller
Figure from ``Limitations of OpenFlow Topology Discovery Protocol,’’ A Azzouni, N. T. M. Trang , R. Boutaba , and G. Pujolle, 16th Annual Mediterranean Ad Hoc Networking Workshop, 2017.

## Slide 30: Bootstrapping
How does a switch communicate with the controller?
OpenFlow uses TCP and (preferably) TLS
Assumes existing IP connectivity

## Slide 31: Out-of-band Mode
Switches connect to controller using separate control network, e.g., Ethernet broadcast domain.
Figure from``Automatic bootstrapping of OpenFlow networks,” S. Sharma, D. Staessens, D. Colle, M. Pickavet and P. Demeester, 19th IEEE Workshop on Local & Metropolitan Area Networks, 2013.

## Slide 32: In-Band Mode
Switches use same network to send control messages and data messages.
A switch must recognize control traffic
Forwarding of control messages must override flows set up by the controller.
Could preconfigure VLAN or MPLS, or use a more complicated bootstrapping process.
Figure from``Automatic bootstrapping of OpenFlow networks,” S. Sharma, D. Staessens, D. Colle, M. Pickavet and P. Demeester, 19th IEEE Workshop on Local & Metropolitan Area Networks, 2013.

## Slide 33: With great power comes …
… many great challenges!
SDN offers network-wide visibility, (programmable) control over switches, and a simple data-plane abstraction. Now, …
  Need to map policies to the low-level API
    Ensure traffic from network A always is screened/scrubbed
    Rules for identifying traffic from A, direct them to scrubber, ensure that this rule is always applied; how to ensure that the implementation matches policy?
  Need to compose modular applications, debug, and verify
    Diff. apps for load balancing, routing, traffic engineering, scrubbing (firewall)
    How to compose or combine? How to debug and verify?

## Slide 34: Policies/Intents
How to specify policy/intent?
  Policies may constitute rules across …
    many switches
    multiple applications
How to handle policy changes?
  Applying policies without disrupting traffic in the network is hard
    May have to change rules across many switches
    … while handling traffic in the network (cannot stop traffic for changes: impractical!)
How to realize policies?
  Hard for developers to handle all the complexities
  Need abstractions to simplify development

## Slide 35: Debugging & verification
Why bother?
  We are good at programming!
  Fact
    Up to 80% of network engineers’ time is spent performing manual configuration§
  Also a fact!
    Developers spend 49% of their time debugging software*
§ONUG, Open Networking Challenges and Opportunities, July 2014.
*Latoza et al., Maintaining Mental Models: a Study of Developer Work Habits. ICSE ’06.

## Slide 36: SDN Debugging
When disaster strikes, how to debug?
  Debugging network applications is hard!
    Inputs to the SDN application are events/packets from the data plane
    Outputs are policies spread across the entire network!

## Slide 37: SDN Verification
How to verify that policies are implemented correctly?
  Leverage network invariants
    Invariant?
      Never changing; a property that always holds!
      No route loops, no blackholes
  Specify the invariants, for instance, to the controller
    When the output of an application violates an invariant, flag it!