## Slide 1: P4 Programming Protocol-Independent Packet Processors
Slides based on materials from Laurent Vanbever and Jennifer Rexford, as modified by Anja Feldmann and Bala Chandrasekaran, and now Bruce Maggs.

## Slide 2: SDN Recap
  Switches and controller communicate via standardized API (e.g., OpenFlow)
  Switches report events to controller
  Controller installs match-action rules in switch forwarding tables
OpenFlow
(API)
Logically-centralized controller
Switches
(Slow but smart)
Key Idea: physically separate control plane from data plane

## Slide 3: OpenFlow Recognized Header Fields
OpenFlow API recognizes header fields for specific protocols
The standard started growing more and more complex
Custom protocols and actions are not supported
P4: Programming Protocol-Independent Packet Processors, P. Bosshart, D. Daly, G. Gibb, M. Izzard, N. McKeown, J. Rexford, C. Schlesinger, D. Talayco, A. Vahdat, G. Varghese, D. Walker. ACM SIGCOMM Computer Communication Review, Volume 44, Issue 3, July 2014, pp. 87–95

## Slide 4: Protocol-Independent Switch Architecture
Make switches protocol independent!
  How? An architectural change is needed.

## Slide 5: Status Quo: Bottom-up design
Custom requirements
Switch OS
Fixed data-plane function ASIC
Legacy Switch
Run-time API
Driver
network
The ASIC (application-specific integrated circuit)
datasheet dictates the rules!

## Slide 6: A better approach: Top-down design
Custom requirements
P4
Switch OS
P4 switch
Run-time API
Driver
network
Feedback
P4 Programmable Device
User/controller dictates the rules

## Slide 7: Protocol-Independent Switch Architecture
Programmable
Parser
Programmable Match-Action Pipeline
Programmable
Deparser
Match-Action Stage
(Unit)
…
…
…
…
…
…
Packets
P4 describes PISA’s behavior

## Slide 8: P4: Goals
Protocol independence
  Programmer defines packet formats (parsing) and processing algorithms (actions).
Target independence
  Low-level hardware organization is not fixed
  Compiler compiles the program for the target device
Consistent control plane interface
  Control plane APIs are automatically generated by the compiler
Reconfigurability
  Data plane program can be changed in the field

## Slide 9: P4: Big picture

## Slide 10: L3 Data Plane Program
Programmable
Parser
Programmable Match-Action Pipeline
Programmable
Deparser
Match-Action
Stage (Unit)
IPv4
IPv6
L2
ACL
(access control list)
Ethernet
MAC
Address
Table
IPv4
Address
Table
IPv6
Address
Table
ACL
Rules

## Slide 11: P4: Language elements
Parsers
Controls
Expressions
Data Types
State machine, bitfield extraction
Tables, Actions, control flow statement
Basic operations and operators
Bitstrings, headers, structures, arrays
Architecture
Description
Extern
Libraries
Programmable blocks and their interfaces
Support for specialized
components

## Slide 12: Example Program from P4 Paper
Add MPLS like tags to route packets in two-level data center “fat-tree” network
Figure from “A Comparative study of data center network architectures,” K. Bilal, S. U. Khan, J. Kolodziej, L. Zhang, S. Madani, N. M. Allah, L. Wang, and D. Chen. In Proceedings of the 26th European Conference on Modeling and Simulation, 2012.
down1
up2
up1
down2

## Slide 13: P4 Program Components
Headers
  specify sequence and structures of fields
Parsers
  specify how to identify headers and header sequences
Tables
  define match fields and which actions to take
Actions
  manipulate data, allowing control plane to influence data plane
Control programs
  Determine the order in which match-action tables are applied to a packet

## Slide 14: P4 Specification
Version 1.0.0 released May 22, 2017
Latest specification (Version 1.2.5, October 11, 2024):
  https://p4.org/wp-content/uploads/2024/10/P4-16-spec-v1.2.5.html
  Cheat sheet:
    https://opennetworking.org/wp-content/uploads/2020/12/p4-cheat-sheet.pdf
  Tutorial:
    https://opennetworking.org/wp-content/uploads/2020/12/P4_D2_East_2018_01_basics.pdf
P4 paper from 2014 uses different syntax
See Version 1.0.5 specification for another implementation of mTag example:
  https://p4.org/p4-spec/p4-14/v1.0.5/tex/p4.pdf

## Slide 15: P4 Types
Basic Types
bit<n>: Unsigned integer (bitstring) of size n
bit is the same as bit<1> <-> bool
int<n>: Signed integer of size n (>=2)
varbit<n>: Variable-length bitstring
bit<48> macAddr;
bit<32> ip4Addr;
int<32> x; int<32> y;
varbit<320> options

## Slide 16: P4 Composite types
Struct
Collection of named members
Tuple
Ordered collection of unnamed members

## Slide 17: P4 Headers (translated from paper)
Similar to a struct in C
Bonus: Hidden “validity” field
extract()
fills the header fields from the packet
If extract() is successful
validity ← true
header ethernet {
bit<48> dst_addr;
bit<48> src_addr;
bit<16> ethertype;
}
header vlan {
bit<3> pcp;
bit<1> cfi;
bit<12> vid;
bit<16> ethertype;
}
header mTag {
bit<8> up1;
bit<8> up2;
bit<8> down1;
bit<8> down2;
bit<16> ethertype;
}
ethernet ethertype 0x8100 or 0x9100, indicates vlan field present
vlan ethertype 0xaaaa indicates tag present

## Slide 18: P4 Headers

## Slide 19: P4 Programs

## Slide 20: Parser uses a state machine

## Slide 21: P4 Parser (translated from paper)
parser tag_parser ethernet {
state start {
transition parse_ethernet;
}
state parse_ethernet {
packet.extract(hdr.ethernet);
transition select(hdr.ethernet.ethertype) {
0x8100: parse_vlan;
0x9100: parse_vlan;
0x800: parse_ipv4;
}
}
state parse_vlan {
packet.extract(hdr.vlan);
transition select(hrd.vlan.ethertype) {
0xaaaa: parse_mTag;
0x800: parse_ipv4;
}
}
state parse_mTag {
packet_extract(hdr.mTag);
transition select(hdr.mTag.ethertype) {
0x800: parse_ipv4;
}
}
}

## Slide 22: P4 Programs

## Slide 23: P4 Tables
Key | Action | Action Data
10.0.1.1/32 | Ipv4_forward | dstAddr= 00:00:00:00:AB:01 port=1
10.0.1.2/32 | drop | 
* | NoAction | 
10.0.1.1
10.0.1.2

## Slide 24: Match-Action Table Operation
Action
Code
Action
Data
Header and
Metatdata Fields
Control Plane
Headers
&
Metadata (e.g., ingress port)
Default Action
Data
Hit
Action
Execution
Metadata
Headers
&
Metadata (output)
Lookup Key
Key | Action | Action Data
Default
Action
Hit/Miss
Selector
Data
Action

## Slide 25: P4 Tables
exact, ternary, lpm, …

## Slide 26: P4 Table (translated from paper)
Table established in each edge switch to add appropriate mTag to each packet (including the up1 tag that the switch itself uses).
Each table entry specifies an exact match on a specific ethernet destination and VLAN ID.
On match, the appropriate tags for reaching the destination are added to the packet.
table mTag_table {
key = {
ethernet.dst_addr: exact;
vlan.vid: exact;
}
actions {
// At runtime, entries are programmed with params
// for the add_mTag action.
add_mTag(params);
}
size = 20000;
}

## Slide 27: P4 Action (translated from paper)
Action add_mTag(up1, up2, down1, down2) {
add_header(mTag);
// Copy VLAN ethertype to mTag
mTag.ethertype = vlan.ethertype
// Set VLAN’s ethertype to signal mTag
vlan.ethertype = 0xaaaa;
mTag.up1 = up1;
mTag.up2 = up2;
mTag.down1 = down1;
mTag.down2 = down2;
// Set the destination egress port as well
metadata.egress_spec = up1;
}

## Slide 28: P4 Statements
return
exit
Control flow
  if … else …
  switch (…) { action1: { ... } action2: { …} }

## Slide 29: P4 Operators

## Slide 30: P4 Variables & Constants

## Slide 31: P4 Variables
Variables cannot be used to maintain state between different network packets!
Stateful constructs?
  Tables
  Externs – architecture-dependent external objects and functions

## Slide 32: P4 Control (notation from paper)
source_check verifies that tags are only seen on ports of switches in core and aggregation levels and strips off mTag.
local_switching checks if destination is a locally connected host.
Matches in table trigger actions.

## Slide 33: Complete P4 Program

## Slide 34: P4 Programs

## Slide 35: Deparser

## Slide 36: Tale of a start-up
Barefoot Networks founded by Martin Izzard, Nick McKeown, Pat Bosshart, Stefanos Sidiropoulos, and Dan Lenoski
Developed “Tofino” series of P4 programmable Ethernet switch ASICS
Acquired by Intel in 2019 for an undisclosed price
In 2023 Intel announced that it was halting production of networking chips